1) Open Pit Mining: Surface

Open-pit mining, open-cut mining or opencast mining is a surface mining technique of extracting rock or minerals from the earth by their removal from an open pit or borrow.

This form of mining differs from extractive methods that require tunneling into the earth such as long wall mining. Open-pit mines are used when deposits of commercially useful minerals or rock are found near the surface; that is, where the overburden (surface material covering the valuable deposit) is relatively thin or the material of interest is structurally unsuitable for tunneling (as would be the case for sand, cinder, and gravel). For minerals that occur deep below the surface - where the overburden is thick or the mineral occurs as veins in hard rock - underground mining methods extract the valued material.

Open-pit mines that produce building materials and dimension stone are commonly referred to as quarries.

Open-pit mines are typically enlarged until either the mineral resource is exhausted, or an increasing ratio of overburden to ore makes further mining uneconomic. When this occurs, the exhausted mines are sometimes converted to landfills for disposal of solid wastes. However, some form of water control is usually required to keep the mine pit from becoming a lake, if the mine is situated in a climate of considerable precipitation or if any layers of the pit forming the mine border productive aquifers.

Open-pit mines are dug on benches, which describe vertical levels of the hole. These benches are usually on four meter to sixty-meter intervals, depending on the size of the machinery that is being used. Many quarries do not use benches, as they are usually shallow.

Most walls of the pit are generally dug on an angle less than vertical, to prevent and minimize damage and danger from rock falls. This depends on how weathered the rocks are, and the type of rock, and also how many structural weaknesses occur within the rocks, such as a fault, shears, joints or foliations.

The walls are stepped. The inclined section of the wall is known as the batter, and the flat part of the step is known as the bench or berm. The steps in the walls help prevent rock falls continuing down the entire face of the wall. In some instances additional ground support is required and rock bolts, cable bolts and shotcrete are used. De-watering bores may be used to relieve water pressure by drilling horizontally into the wall, which is often enough to cause failures in the wall by itself.[1]

A haul road is usually situated at the side of the pit, forming a ramp up which trucks can drive, carrying ore and waste rock.

Waste rock is piled up at the surface, near the edge of the open pit. This is known as the waste dump. The waste dump is also tiered and stepped, to minimize degradation.

Ore which has been processed is known as tailings, and is generally a slurry. This is pumped to a tailings dam or settling pond, where the water evaporates. Tailings dams can often be toxic due to the presence of unextracted sulfide minerals, some forms of toxic minerals in the gangue, and often cyanide which is used to treat goldore via the cyanide leach process. This toxicity can harm the surrounding environment

2) Dredging: surface

Dredging is an excavation activity or operation usually carried out at least partly underwater, in shallow seas or fresh water areas with the purpose of gathering up bottomsediments and disposing of them at a different location. This technique is often used to keep waterways navigable.

It is also used as a way to replenish sand on some public beaches, where sand has been lost because of coastal erosion. Dredging is also used as a technique for fishing for certain species of edible clams and crabs, see fishing dredge.

A dredger (or “dredge” as is the general usage in the Americas) is any device, machine, or vessel that is used to excavate and remove material from the bottom of a body of water. For example, a scoop attached to the end of a rope or pole by which a man can draw sediments up from the bottom of a pond is a dredger. Developing this idea further, a motorized crane equipped with a drag bucket or clamshell (grabber) that is used to scoop material from the bottom of a body of water is also a dredger. The crane could be located on the bank, or perhaps mounted on a barge. If the crane is mounted on a barge, the entire vessel is referred to as a dredger.

The process of dredging creates spoils (excess material), which are carried away from the dredged area. Dredging can produce materials for land reclamation or other purposes (usually construction-related), and has also historically played a significant role in gold mining. Dredging can create disturbance in aquatic ecosystems, often with adverse impacts.

3) Strip Mining: surface

"Strip mining" is the practice of mining a seam of mineral, by first removing a long strip of overlying soil and rock (the overburden). It is most commonly used to mine coal and lignite (brown coal). Strip mining is only practical when the ore body to be excavated is relatively near the surface. This type of mining uses some of the largest machines on earth, including bucket-wheel excavators which can move as much as 12,000 cubic meters of earth per hour.

There are two forms of strip mining. The more common method is "area stripping", which is used on fairly flat terrain, to extract deposits over a large area. As each long strip is excavated, the overburden is placed in the excavation produced by the previous strip.

"Contour stripping" involves removing the overburden above the mineral seam near the outcrop in hilly terrain, where the mineral outcrop usually follows the contour of the land. Contour stripping is often followed by auger mining into the hillside, to remove more of the mineral. This method commonly leaves behind terraces in mountainsides.

4) Mountain Top Removal: surface

"Mountaintop removal mining" (MTR) is a form of coal mining that uses explosives to blast "overburden" off the top of some Appalachian mountains. Excess mining waste or "overburden" is dumped by large trucks into fills in nearby hollow or valley fills. MTR involves the mass restructuring of earth in order to reach the coal seam as deep as 400 feet (120 m) below the surface. Mountaintop removal replaces the original steep landscape with a much flatter topography, which may be suited to various different uses. Economic development attempts on reclaimed mine sites include prisons such the Big Sandy Federal Penitentiary in Martin County, Kentucky, small town airports, golf courses such as Twisted Gun in Mingo County, West Virginia and Stonecrest Golf Course in Floyd County, Kentucky, as well as industrial scrubber sludge disposal sites, solid waste landfills, trailer parks, explosive manufacturers, and storage rental lockers.

The technique has been used increasingly in recent years in the Appalachian coal fields of West Virginia, Kentucky, Virginia and Tennessee in the United States. The profound changes in topography and disturbance of pre-existing ecosystems have made mountaintop removal highly controversial.

Advocates of mountaintop removal point out that once the areas are reclaimed as mandated by law, the technique provides premium flat land suitable for many uses in a region where flat land is at a premium. They also maintain that the new growth on reclaimed mountaintop mined areas is better able to support populations of game animals.

Critics contend that mountaintop removal is a disastrous practice that benefits a small number of corporations at the expense of local communities and the environment. A U.S. Environmental Protection Agency(EPA) environmental impact statement finds that streams near valley fills sometimes may contain higher levels of minerals in the water and decreased aquatic biodiversity. The statement also estimates that 724 miles (1,165 km) of Appalachian streams were buried by valley fills from 1985 to 2001.

Blasting at a mountaintop removal mine expels dust and fly-rock into the air, which can then disturb or settle onto private property nearby. This dust may contain sulfur compounds, which some claim corrode structures and tombstones and is a health hazard.

Although MTR sites are required to be reclaimed after mining is complete, reclamation has traditionally focused on stabilizing rock and controlling erosion, but not always on reforesting the area. Quick-growing, non-native grasses, planted to quickly provide vegetation on a site, compete with tree seedlings, and trees have difficulty establishing root systems in compacted backfill. Consequently, biodiversitysuffers in a region of the United States with numerous endemic species. Erosion also increases, which can intensify flooding. In the Eastern United States, the Appalachian Regional Reforestation Initiative works to promote the use of trees in mining reclamation.

5) Room and Pillar: subsurface

Room and pillar (variant of breast stoping), also called pillar and stall, is a mining system in which the mined material is extracted across a horizontal plane, creating horizontal arrays of rooms and pillars. The ore is extracted in two phases. In the first, "pillars" of untouched material are left to support the roof overburden, and open areas or "rooms" are extracted underground; the pillars are then partially extracted in the same manner as in the "Bord & Pillar method". The technique is usually used for relatively flat-lying deposits, such as those that follow a particular stratum.

The room and pillar system is used in mining coal, iron and base metals ores, particularly when found as manto or blanket deposits, stone and aggregates, talc, soda ash and potash.

The key to successful room and pillar mining is in the selection of the optimum pillar size. In general practice, the size of both room and pillars are kept almost equal, while in Bord & Pillar, pillar size is much larger than bord (gallery). If the pillars are too small the mine will collapse, but if they are too large then significant quantities of valuable material will be left behind, reducing the profitability of the mine. The percentage of material mined varies depending on many factors, including the material mined, height of the pillar, and roof conditions; typical values are: stone and aggregates 75 percent, coal 60 percent, and potash 50 percent

Room and pillar mining is one of the oldest mining methods. Early room and pillar mines were developed more or less at random, with pillar sizes determined empirically and headings driven in whichever direction was convenient.

Random mine layout makes ventilation planning difficult, and if the pillars are too small, there is the risk of pillar failure. In coal mines, pillar failures are known as squeezes because the roof squeezes down, crushing the pillars. Once one pillar fails, the weight on the adjacent pillars increases, and the result is a chain reaction of pillar failures. Once started, such chain reactions can be extremely difficult to stop, even if they spread slowly

Room and pillar mines are developed on a grid basis except where geological features such as faults require the regular pattern to be modified. The size of the pillars is determined by calculation. The load-bearing capacity of the material above and below the material being mined and the capacity of the mined material itself will determine the pillar size.

If one pillar fails and surrounding pillars are unable to support the area previously supported by the failed pillar they may in turn fail. This could lead to the collapse of the whole mine. To prevent this the mine is divided up into areas or panels. Pillars known as barrier pillars separate the panels. The barrier pillars are significantly larger than the "panel" pillars and are sized to allow them to support a significant part of the panel and prevent progressive collapse of the mine in the event of failure of the panel pillars

6) Longwall Mining: subsurface

Longwall mining is a form of underground coal mining where a long wall of coal is mined in a single slice (typically 0.6–1.0 m thick). The longwall panel (the block of coal that is being mined) is typically 3–4 km long and 250–400 m wide.

The basic idea of longwall mining was developed in England in the late 17th century. Miners would undercut the coal along the width of the coal face, removing coal as it fell, and using wooden props to control the fall of the roof behind the face. this was known as the Shropshire method of mining. While the technology has changed considerably, the basic idea remains the same, to remove essentially all of the coal from a broad coal face and allow the roof and overlying rock to collapse into the void behind, while maintaining a safe working space along the face for the miners.

Starting around 1900, mechanization was applied to this method. By 1940, some referred to longwall mining as "the conveyor method" of mining, after the most prominent piece of machinery involved. Unlike earlier longwall mining, the use of a conveyor belt parallel to the coal face forced the face to be developed along a straight line. The only other machinery used was an electric cutter to undercut the coal face and electric drills for blasting to drop the face. Once dropped, manual labor was used to load coal onto the conveyor parallel to the face and to place wooden roof props to control the fall of the roof.

Such low-technology longwall mines continued in operation into the 1970s. The best known example was the New Gladstone Mine near Centerville, Iowa "one of the last advancing longwall mines in the United States". This longwall mine did not even use a conveyor belt, but relied on ponies to haul coal tubs from the face to theslope where a hoist hauled the tubs to the surface.

Longwall mining has been extensively used as the final stage in mining old room and pillar mines. In this context, longwall mining can be classified as a form of retreat mining.

MISSION MINING!!

Directions:

1) Read your assigned mining technique.

2) Jot down important notes and facts about your mining technique.

3) After 10 minutes, gather in a group so that every mining technique is represented.

4) Take turns sharing out important information on your mining technique. Please take notes on others mining techniques. You are responsible for learning this information.

5) After sharing out of information has occurred, your group must work together to create a graphic organizer that best represents the information presented by members of the group. Your graphic organizer can be of any type, but must represent the information in a clear, concise way. And, it must be extremely easy to read.

6) Hang your graphic organizer anywhere in the class.

7) Now, your group needs to brainstorm and come up with at least three (3) ways the environment is harmed with these mining techniques.

8) Pick two of your three environmental effects of mining and write them on the huge poster titled “Environmental Hazards of Mining” located in the front of the class.